## Slide 1: PKCS#15 - an ICC File Format Recommendation
Magnus Nyström
RSA Laboratories
PKCS Workshop October 1998

## Slide 2: Agenda
Introduction, motivation
The proposal - an overview
Issues
Experiences from the SEIS work Hans Nilsson, AU Systems AB
Experiences from DC/SC Scott Guthery, Microsoft
Discussion

## Slide 3: Introduction
What is a ‘card format’?
  A detailed description on how certain higher-level abstractions such as keys and certificates is represented on a particular card in terms of files, directory structure, etc
  It can also contain recommendations about commands to use and access control rules

## Slide 4: Introduction, cont.
Are there any standardized formats?
  ISO has laid out the foundations in ISO 7816-4, defining file types and commands for accessing them
  There is no generally recognized standard format

## Slide 5: Introduction, cont.
So, card issuers have implemented their own formats, bound to their applications
There are standardized APIs aimed towards tokens like smart cards
But since there is no standard smart card format, users can’t receive full benefit from them

## Slide 6: Conclusion
A common card file format recommendation offers interoperability benefits for:
  -Users (Card Holders)
  -Card Issuers
  -Application Vendors
This is the goal of PKCS#15 -
The ICC File Format Recommendation

## Slide 7: PKCS#15
Part II: An Overview of the Proposal

## Slide 8: Format Characteristics and Requirements
Useful on both crypto-capable cards as well as stored-value cards
Supports multiple applications
Supports whole domain of PKCS#11 objects

## Slide 9: Format Characteristics and Requirements, cont.
Straightforward to do PKCS#11 interface, but not tied to PKCS#11
Profiling possible
Based on, and an application of, ISO 7816

## Slide 10: Card layout
MF
DF(PKCS15)
ODFs
Object
More Objects
Other DFs
TokenInfo
PinInfo

## Slide 11: The TokenInfo file
Contains information about the token per se and its capabilities (and peculiarities)
Corresponds roughly to PKCS#11 CK_TOKEN_INFO

## Slide 12: ODF - Object Directory Files
Contains
  pointers to all objects on the card
  their attributes (or pointers to their attributes)

## Slide 13: Pin Information File
Applications needs to know:
  If a PIN is case-sensitive
  If a given PIN needs to be ‘padded’
If several PINs, there is a need
  To associate PINs with objects
  To know if a PIN is local or global

## Slide 14: Token Object Files
Contains values for one or more token objects
Could contain their other attributes as well
Need not be in same DF as ODF

## Slide 15: Summary
PKCS#15:
  enables true card interoperability between card-aware applications
  allows profiling for particular uses, like Electronic Identity cards
  is based on PKCS#11 objects
  is tentatively targeted for v1.0 in Q1 1999

## Slide 16: PKCS#15
Part III: Issues and Discussion

## Slide 17: Issues (in no particular order)
How to recognize supported algorithms
How to recognize supported commands?
# of PINs? PKCS#11 only supports one.
Encoding of data: ASN.1/[PD]er or XDR or other (or several)?

## Slide 18: Issues, cont.
Relationship to other initiatives (MultOS, PC/SC (CAPI), JavaCard)?
Support for pure memory cards?
Specific card implementation details?
CA certificates on the card?
Several ODFs (keys, certs, etc) or none (implicit searching via File Identifiers)?

## Slide 19: How to proceed?
Suggest a separate mailing list, e.g. pkcs-15@rsa.com
Goal is to reach a ‘final’ version during Q1 ‘99
Comments, feedback is solicited and welcome

## Slide 20: An Alternative: Formal profiling
-- Information object classes
PKCS15-PROFILE ::= CLASS {
&id OBJECT IDENTIFIER UNIQUE,
&Type
WITH SYNTAX {
&Type IDENTIFIED BY &id
}
PROFILE-PARAMETERS ::= CLASS {
&privKeyLength INTEGER,
&noPrivateKeys INTEGER,...
}
WITH SYNTAX {
THE NUMBER OF DATA OBJECTS ARE &noDataObjects
THE NUMBER OF PRIVATE KEYS IS &noPrivateKeys
THE PRIVATE KEY LENGTH SHALL BE &privKeyLength
THE OBJECT IDENTIFIER IS &oid
...
}

## Slide 21: Alternative: Formal profiling, cont.
generic-pkcs15-profile { PKCS15-PARAMETERS : params } PKCS15-PROFILE ::= {
{
ODF { params }
IDENTIFIED BY { params.&oid }
}
eid-params PROFILE-PARAMETERS ::= {
THE NUMBER OF DATA OBJECTS IS 0
THE NUMBER OF PRIVATE KEYS IS 2
THE PRIVATE KEY LENGTH SHALL BE 1024
THE OBJECT IDENTIFIER IS { eid-oid }
}
eid-profile PKCS15-PROFILE ::=
generic-pkcs15-profile { eid-params }

## Slide 22: Alternative: Formal Profiling, cont.
ODFContents {PKCS15-PARAMETERS params} ::= SEQUENCE {
version INTEGER,
privateKeys PrivateKeys {params}(SIZE(&params.noPrivKeys),
publicKeys PublicKeys {params},
secretKeys SecretKeys {params},
certificates Certificates {params},
dataObjects DataObjects {params},
}
PKCS15PrivateKey {PKCS15-PARAMETERS : params }::= SEQUENCE {
key INSTANCE OF PKCS15-KEY {params}
pKCS15CommonObjectAttributes PKCS15CommonObjectAttributes,
pKCS15CommonKeyAttributes PKCS15CommonKeyAttributes,
pkCS15CommonPrivateKeyAttributes PKCS15CommonPrivateKeyAttributes
}

## Slide 23: Alternative: Formal Profiling, cont.
PKCS15PrivateRSAKey {PKCS15-PARAMETERS : params }::= SEQUENCE {
modulusLength INTEGER { params.&privKeyLength },
subjKeyHash OCTET STRING,
path [1] IMPLICIT PKCS15Path OPTIONAL,
value [2] IMPLICIT PKCS15RSAPrivateKey OPTIONAL
} (WITH COMPONENTS {..., path PRESENT, value ABSENT} |
WITH COMPONENTS {..., path ABSENT, value PRESENT})

## Slide 24: Alternatives to ASN.1: SSL notation
enum { xx_rsa_private_key(1), xx_ec_key(2), xx_certificate(3),
xx_secret_key(4) , (255) } XXObjectType;
struct {
/* something */
} XXRSAPrivateKey;
struct {
/* something */
} XXECKey;
struct {
/* something */
} XXCertificate;

## Slide 25: Alternatives to ASN.1, cont.
struct {
/* something */
} XXSecretKey;
struct {
XXObjectType type;
switch (type) {
case xx_rsa_private_key: XXRSAPrivateKey;
case xx_ec_key: XXECKey;
case xx_certificate: XXCertificate;
case xx_secret_key: XXSecretKey;
}
} XXObject;
struct {
XXObject objects<0..2^16-1>
} XXWholeStuff;