## Slide 1: RC6—The elegant AES choice
Ron Rivest rivest@mit.edu
Matt Robshaw mrobshaw@supanet.com
Yiqun Lisa Yin yiqun@nttmcl.com

## Slide 2: RC6 is the right AES choice
Security
Performance
Ease of implementation
Simplicity
Flexibility

## Slide 3: RC6 is simple: only 12 lines
B = B + S[ 0 ] D = D + S[ 1 ] for i = 1 to 20 do { t = ( B x ( 2B + 1 ) ) <<< 5 u = ( D x ( 2D + 1 ) ) <<< 5 A = ( ( A  t ) <<< u ) + S[ 2i ] C = ( ( C  u ) <<< t ) + S[ 2i + 1 ] (A, B, C, D) = (B, C, D, A) } A = A + S[ 42 ] C = C + S[ 43 ]

## Slide 4: Simplicity
Facilitates and encourages analysis
  allows rapid understanding of security
  makes direct analysis straightforward (contrast with Mars and Twofish)
Enables easy implementation
  allows compilers to produce high-quality code
  obviates complicated optimizations
  provides good performance with minimal effort

## Slide 5: RC6 security is well-analyzed
RC6 is probably most studied AES finalist
  RC6 is based on RC5
  RC6 analysis builds directly on RC5 analysis
  original RC6 analysis is very detailed
  RC6 simplified variants studied extensively
  small-scale versions allowed experimentation

## Slide 6: RC6 key schedule is rock-solid
Studied for more than six years
Secure
  thorough mixing
  one-way function
  no key separation (cf. Twofish)
  no related-key attacks (cf. Rijndael)

## Slide 7: Original analysis still accurate
RC6 meets original design criteria
Security estimates from 1998 still good today; independent analyses supportive.
Secure, even in theory, even with analysis improvements far beyond those seen for DES during its lifetime
RC6 provides a solid, well-tuned margin for security

## Slide 8: 32-bit Performance
Excellent performance
32-bit CPUs are
  NIST reference platform
  a significant fraction of installed computers throughout the AES lifetime
  becoming more prevalent in cheaper devices (e.g. ARM)

## Slide 9: Smart Card Suitability
RC6 fits in the cheapest smart cards, and well-suited for many (e.g. ARM processor)
Bandwidth, not CPU, likely to be most significant bottleneck
8-bit CPUs will become far less important over the AES lifetime

## Slide 10: Performance on 64-bit CPUs
Generally good 64-bit performance
IA64-performance only fair but anomalous--slower than Pentium!
  Note 3x improvement with IA64++
Future chips will optimize AES
In addition, RC6 gains dramatically with multi-block processing compared to other schemes

## Slide 11: Major Trends: Java and DSPs
Increasing use of Java
  for e-commerce and embedded apps.
  RC6 provides excellent speed with minimal code size and memory usage
Increasing use of DSP chips
  likely to be more significant than IA64 or 8-bit processors
  RC6 gives excellent performance

## Slide 12: Flexibility
RC6 is fully parameterized
  key size, number of rounds, and block length can be readily changed
  well-suited for hash functions
RC6 is only AES finalist that naturally gives DES and triple-DES compatible variants (64-bit blocks)

## Slide 13: How do we grade candidates?
Security (corroborated)
Performance (speed+memory)
  32-bit (30%)
  Java (20%)
  DSP (15%)
  64-bit (15%)
  Hardware (15%)
  8-bit (5%)
Ease of implementation
Simplicity
Flexibility
Overall: 40/25/15/10/10

## Slide 14: Conclusions
RC6 is a simple yet remarkably strong cipher
  good performance on most important platforms
  simple to code for good performance
  excellent flexibility
  the most studied finalist
  the best understood finalist
RC6 is the secure and “elegant” choice for the AES

## Slide 15: (The End)