## Slide 1: RSA Laboratories’ PKCS Series - a Tutorial
PKCS #15 v1.0
Magnus Nyström
October, 1999

## Slide 2: Agenda
Background - the Need for Standardization
Previous Efforts
An Overview of PKCS #15
Summary & Future Work

## Slide 3: Background
There is a need for standardization of the format of cryptographic credentials stored on cryptographic tokens, if one wants portability

## Slide 4: Lot of buzzwords...

## Slide 5: Definitions
What is a “cryptographic token”?
  We define it as: A portable device capable of storing cryptographic credentials identifying its owner
What are “Cryptographic credentials”?
  Keys and Certificates

## Slide 6: Background
What is a token “format”?
  A detailed description of how certain higher-level abstractions such as keys and certificates are represented on a token in terms of e.g.
    data structures
    file contents
    directory structures
    etc.

## Slide 7: Background, Continued
Why standardize a token format?
  Without a standardized token format there will be no interoperability
Are not APIs enough (e.g. PKCS #11, OpenCard…)?
  Standardized APIs are neither necessary nor sufficient for token portability, but they help 3rd party vendors

## Slide 8: I still don’t get it...

## Slide 9: Here’s the problem... (from S.Guthery)
Application is tied to particular cards so ….
Cardholder is tied to particular applications.
Reader
Card
Token (Card)-aware application
Standard API

## Slide 10: …and a solution!
IC Card
Application
A
IC Card
Application
C
Standard API
Standard API
IC Card
Application
B
Standard API
PC/SC
PKCS #15
E.g.
PKCS #11

## Slide 11: PKCS #15 is...
…an attempt to eliminate differences between tokens with respect to certain security-related information
…a ‘token edge’ specification for the exchange of information between a host and a token
...based on, and an application of, ISO/IEC 7816-4, -5 and -6.

## Slide 12: PKCS #15 is...
…not biased towards particular IC cards or tokens
…for the benefit of token-holders and vendors of token-aware applications
…supported by major vendors and consortiums like WAP, Microsoft, Netscape and Apple

## Slide 13: PKCS #15 Goal
To enable portability of personal credentials stored on cryptographic tokens across computer applications

## Slide 14: Previous work
DC/SC - CertCo/GemPlus/Litronics initiative
  Storage of digital certificates on smart cards
  Designed for multi-application cards
  Folded into SEIS

## Slide 15: The DC/SC format
Cert1 info
Cert2 info
MF
DF 1
DF 2

## Slide 16: Previous work
SEIS - Swedish initiative (http://www.seis.se)
  Pre-dates DC/SC
  EID application
  Promoted to Swedish standard SS 614330 in September 1998
  Not as general as PKCS #15

## Slide 17: The SEIS format
PIN info
Key info
Cert info
PIN file
DF(EID)
Key 1
Cert 1
AUF

## Slide 18: An overview of PKCS #15

## Slide 19: PKCS #15 Characteristics
Useful on a wide range of tokens
No need to modify existing tokens
Supports multiple applications
Supports whole domain of PKCS #11 objects (straightforward to do PKCS #11 interface but not tied to PKCS #11)
Profiling possible (e.g. EID)

## Slide 20: IC Card layout
MF
DF(PKCS15)
ODF
PrKDFs
CDFs
Other DFs
TokenInfo
AODFs
Objects

## Slide 21: The TokenInfo file
Contains information about the token per se and its capabilities (and peculiarities)
Corresponds roughly to PKCS#11 CK_TOKEN_INFO

## Slide 22: ODF (Object Directory File)
Contains pointers to other directory files:
  PrKDFs
  PuKDFs
  SKDFs
  CDFs
  DODFs
  AODFs

## Slide 23: AODFs (Authentication Object Directory Files)
Application needs to know:
  Which authentication methods are used to protect certain objects
If the authentication method is PIN- based, there is a need to:
  Associate PINs with objects
  Record PIN information: case-sensitive, numeric, length, lifetime, ...

## Slide 24: PrKDFs (Private Key Directory Files)
Contain attributes for one or more private keys known to the application
Keys need not be in same DF as the PrKDFs
Associates keys with authentication objects and certificates

## Slide 25: CDFs (Certificate Directory Files)
Contain attributes for one or more certificates known to the application
Certificates need not be in same DF as the CDFs
Associates certificates with private keys

## Slide 26: An Example - simple EID
ODF
AODF
PrKDF
CDF
PrKDF
Key 1 info
Key 2 info
Key 1
Key 2
CDF
Cert 1 info
Cert 2 info
Cert1
Cert2
AODF
PIN1 info
PIN2 info

## Slide 27: Summary
Format standardization is required for portability of credentials stored on tokens
PKCS#15 is a standard aimed to help meet this requirement, which:
  builds on previous work, e.g. PKCS #11
  allows profiling for particular uses, like Electronic Identification (EID) applications

## Slide 28: Results?
The EID profile of PKCS #15...
  ...has been chosen as the token format for WAP’s SIM module (WIM)
  …has been chosen as the card-format for the Finnish national EID card
  ...is being considered for inclusion in the German DIN digital signature card specification
  …has been tested in interoperability workshops

## Slide 29: Future work
PKCS #15 does not solve the problems of a non-standardized command set and access control model
  A card adaptation layer is still needed
  Combining PKCS #15 with, e.g. ISO/IEC 7816-4, -8 and -9 could eliminate this need
  Another possibility is “Security Service Descriptors” (like in DIN NI-17.4)
What is the equivalent of PKCS #15 for a JavaCard or a MultOS card?

## Slide 30: Part II: PKCS #15 v1.1

## Slide 31: Some Limitations in PKCS #15 v1.0
Many organizations cannot afford an infrastructure with cards and readers or would prefer to start with software-only tokens
Memory cards are very popular in some countries
No reason why PKCS #15 should not include support for these tokens

## Slide 32: Overview of the forthcoming proposal
Added support for integrity- and confidentiality- protection of tokens
Whole objects may be protected, or just some attributes (I.e. the value of the object)
Added possibility to store thumbprint of all external objects, not just certificates

## Slide 33: The PKCS15Token Type
tokenInfo
KeyMgmtInfo
Objects
Components of token info
Key mgmt info table
Pointers to objects
The tokenInfo field consists of all components from the current TokenInfo type
Objects are the same as in the current object directory file (ODF)
This type may itself be integrity protected

## Slide 34: Key Management Info
One or several pairs of:
A recipient info is the same as in PKCS #7, but a passwordRecipientInfo has been added
keyId
keyInfo
Integer identifier
RecipientInfo

## Slide 35: Password Based Recipient Info
The nesting allows several objects to be protected with the same password
Version
Hints
PBEAlgorithm
keyID
v1
E.g. “My Bank password”
E.g. from PKCS #5
Nested KeyID pointing
back to a RecipientInfo

## Slide 36: Integrity Protected Data
Version
KeyID
Algorithm
content
MAC
v1
Pointer to Key mgmt
E.g. hMAC
What’s protected
MAC value

## Slide 37: Confidentiality Protected Data
Version
KeyID
Algorithm
content
v1
Pointer to Key mgmt
E.g. DES-EDE
What’s protected

## Slide 38: Protection of of Object Values
A sequence of objects, or an object value itself may now be
  directly stored (I.e. “inline”)
  indirectly stored (pointed to)
  direct-protected (confidentiality protected, directly stored)
  indirect-protected (confidentiality protected, and pointed to)

## Slide 39: Software Tokens
Top-level structure will be PKCS15Token
  May or may not be integrity protected
  Will contain all other objects, or pointers (urls) to them
  Private objects will be encrypted
  All keys will be in a key management table (except perhaps for the outermost integrity protection key)

## Slide 40: Memory cards and other simple H/W tokens
The EF(ODF) may or may not be integrity protected.
Files containing private objects will, most likely, be encrypted
As an alternative, a complete PKCS15Token may be stored on the card/H-W token as one file

## Slide 41: Summary
The proposal extends the capacity of PKCS #15, it does not make any existing applications incompatible
The proposal allows tokens not capable of protecting private objects themselves to store such objects in a secure manner
It is still just a proposal

## Slide 42: Other possible enhancements
Command mappings (in an attempt to get rid of specific card layers)?
ACL mappings (for easier knowledge of rights)?
Support for biometric authentication methods?
Support for external/internal AUTH commands/methods/protocols?

## Slide 43: Other possible enhancements, continued
Should it be possible to find PKCS #15 applications on an IC Card without using the PKCS #15 AID? If so, how?

## Slide 44: Time plan
1st draft of PKCS #15 v1.1 will be submitted late October/early November
A 2nd draft is expected early in January
v1.1 expected in February 2000

## Slide 45: How can I help?

## Slide 46: Contact Us!
As usual, send comments and suggestions to
  pkcs-tng@rsasecurity.com, or
  pkcs-editor@rsasecurity.com